| NRCS Natural Resources Conservation Service | Prescribed Burning Prescribed Burning Job Sheet 338 |
| --- | --- |
| May 2011 |
| Client/Operating Unit: |  | Tract: |  | Farm No.: |  | Field No.: |  |
| Farm/Ranch Location: |  | County: |  | SWCS/HU Code: |  | Date: |  |
| Program: |  | Contract Item #: |  | Planned Installation Date: |  |

| General Description of Area to be Burned |
| --- |
| Dominant Vegetation Type: (Check One) Short Grass Tall Grass Mixed Grass and Shrubs PJ Woodland Forest High Volatility Dense Vegetation | Acres: |  |
| Legal Description: | Section: |  | Township: |  | Range: |  |
| GPS Coordinates (if known): |  |
| Written Directions from nearest town: (Be specific so that these directions can be read to emergency personnel if needed) |
| Projected Date of Burn: |  | Date of Previous Burn: |  |
| Objectives to be Accomplished through the Prescribed Burn (Check all that apply) |
| To control undesirable vegetation. Prepare sites for planting or seeding. Control plant disease. Reduce wildfire hazards. Improve wildlife habitat. | Improve plant production quantity and/or quality. Remove slash and debris. Enhance seed and seedling production. To facilitate distribution of grazing and browsing animals. Restore and maintain ecological sites. |
| Notifications: (Responsibility of Client). |
| When burning on non-federal lands Contact New Mexico State Forestry at: | Location | Phone Number |
| Fire Departments | Phone Number | Date, Time and Person Notified |
| Adjoining Landowners | Phone Number | Date and Time of Notification |
| Others, as Needed (Sheriff, SHP, Air Quality, Utility Companies, Oil and Gas Leases) | Phone Number | Date, Time and Person Notified |
| NM Air Quality Smoke Desk | (800) 224-7009, ext. 4330 (or ask for Smoke Management) |  |
| Pre-Burn Preparations – Describe management needed prior to burn in order to successfully accomplish burn and meet objectives. (Deferred grazing to build fuel loads; prescribed grazing to reduce fuel loads; fireguard preparation; burning of bush piles; moving brush piles, etc.) |
| Firebreak Types (include locations on map) | Dimensions | Preparation / Installation |
|  |  | Dates | Equipment needed |
| Smoke Management Considerations – Refer to New Mexico Smoke Management Rules: |
| Sensitive Areas Identified | Direction from Burn Area | Distance to Area |
| Other Smoke Management Considerations SMP I SMP II (Category Day, hours of burning; local ordinances; dispersion conditions; applying various smoke control strategies such as avoidance ( burn when the wind is blowing away from all smoke-sensitive areas, avoid burning if temperature inversions are present, etc.), dilution (reducing smoke concentrations by burning during good and rapid dispersion conditions, burning at slower rates, burning smaller areas, burning lighter fuel loads if the desired results can be achieved by doing so, burning mid-day rather than late afternoon or evening, etc.), emission reduction (minimize smoke output per unit area by utilizing effective firing techniques such as backfires, by proper scheduling for periods when duff and larger fuels are too wet to burn, by removing larger materials from the area to reduce emissions from residual smoldering smoke, etc.); burning under favorable moisture conditions; “mop-up” quickly to reduce residual smoldering smoke; etc.) |
| Ventilation Category Day | Preferred Category Day |  | Actual Category Day (day of burn) |  |
| Dispersion Conditions | Preferred Dispersion Conditions |  | Actual Dispersion Conditions (day of burn) |  |
| Additional Smoke Management Notes: Burn ignition not before 1 hour after sunrise and not after 1 hour before sunset unless emergency dictates. No ignition in poor ventilation or red flag conditions. |

| Pre-Burn Checklist - The following items should be addressed prior to implementing burn and appropriate action taken. Protection of facilities and/or special areas should be documented and included on map. |
| --- |
|  | Action needed / Recommended | Accomplished (Client Checks) |
| Liability Protection and Notifications |  |  |
| Pens/Barns |  |  |
| Oil/Gas/Pipelines/ Utility Structures |  |  |
| Fences |  |  |
| Homes/Cabins |  |  |
| Windmills |  |  |
| Watering Facilities |  |  |
| Feeding Facilities/Hay Storage |  |  |
| Equipment/Vehicles |  |  |
| Wildlife Habitat Areas |  |  |
| Critical Eroding Areas |  |  |
| Livestock |  |  |
| Volatile Fuels |  |  |
| Other Areas Desired for Protection |  |  |
| Inspection of Firebreaks (Check all firelines for “fuel bridging” before starting the burn. |  |  |

| Fuel Conditions Needed to Accomplish the Burn and Achieve Objectives – Planning should begin early enough to achieve adequate fuel conditions needed to accomplish the burn. Special management needed to achieve this should be addressed in pre-burn preparations. |
| --- |
|  | Prescription | Actual (day of burn) |
| Fine Fuel Amount (lbs/ac) 1 |  |  |
| Continuity 1 | Good Fair Poor | Good Fair Poor |
| 100 hour fuel moisture (% dry wt. Basis) 2 |  |  |
| 10 hour fuel moisture (% dry wt. Basis) 2 |  |  |
| Mulch Load (lbs./ac) 2 |  |  |
| Mulch Depth (inches) 2 |  |  |
| Mulch moisture content (%) 2 |  |  |
| 1 – Required entry ; 2 – As needed (Mature Juniper, PJ, and conifer forest)( |
| Weather Conditions - Prescription |
| Prescription | Firebreaks or Backfires | Prescribed Burn |
|  | Optimum | Maximum Range | Optimum | Maximum Range |
| Wind Speed |  |  |  |  |
| Wind Direction |  |  |  |  |
| Relative Humidity |  |  |  |  |
| Air Temperature |  |  |  |  |
| Duff and Soil Surface | Dry Damp Wet | Dry Damp Wet |
| Soil Profile | Dry Damp Wet | Dry Damp Wet |
| Risk of Spot fires | High Med Low | High Med Low |
| On Site Measured Weather and Fuel | High | Low |
| Wind Speeds |  |  |
| Wind Direction |  |  |
| Temperatures |  |  |
| Relative Humidity |  |  |
| Other as needed |  |  |
| Source of Data |  |  |
| Fuel Load in Pounds |  |  |
| Weather Forecasts – (Responsibility of Client) Timing of burning is dependent upon prescribed weather conditions. Both the 7 day and 24 hour forecasts MUST be checked and documented in order to plan burn according to prescription. |
| Forecasted Item | Seven (7) day Forecast | Twenty-Four (24) hour Forecast |
| Predicted Windshifts |  |  |
| Wind Speeds |  |  |
| Wind Direction |  |  |
| Temperatures |  |  |
| Relative Humidity |  |  |
| Other as needed |  |  |
| Source of Data |  |  |
| Equipment Needs and Crew Member Responsibilities Checklist |
| – Various types of equipment may be needed in order to have a safe and successful burn. The following checklist should be used to inventory available equipment and plan for needed equipment. All equipment should be tested prior to starting the fire. It is also a good idea to have back-up equipment on hand. |
| Equipment Items | Equipment Suggestions | Amount On-Hand | Amount Needed | Comments / Other Considerations | Available Day Of Burn |
| Hand Tools | Drip torch(es) | Used for lighting the firelines; should be held upright to prevent dripping fuel or extinguished; air vent should be adjusted for fine fuel conditions and walking pace |  |  |  |  |
|  | Flapper(s) | Place and hold over fire or use like a mop over an area to smother flames – Do Not Flap Or Swat! |  |  |  |  |
|  | Shovel(s) | Clear small areas of firebreak; smother flames; place dirt over flames |  |  |  |  |
|  | Rake(s) (McLeod rakes, garden rakes, etc.) | Clear areas or widen firebreaks, especially in wooded areas; spread fire by dragging fine fuel; prevent fire from spreading by dragging fine fuel & fire back on itself |  |  |  |  |
|  | Backpack pump(s) / Sprayer(s) | Used for putting fire out especially in areas where larger sprayers or equipment is hard to get in |  |  |  |  |
|  | Leaf Blower(s) | Mainly used in timbered areas to blow a clean line to bare soil through leaf litter; can also blow out small backfires or small flank fires |  |  |  |  |
|  | Flags for flagmen | To regulate traffic on roads or highways when smoke reduces visibility |  |  |  |  |
|  | Chainsaw(s) / Tree saw(s) | Helpful for cutting down snags and hollow trees before or after the burn |  |  |  |  |
| Large equipment | Pumper truck(s) | Good to have on standby should the fire escape; source of additional water |  |  |  |  |
|  | Tractor(s) / Maintainer(s) | Good to have on standby should the fire escape; can blade new firebreaks to contain an escape; can blade out or cover small fires to put them out |  |  |  |  |
|  | Livestock sprayer(s) | Helpful for putting out small escapes; can be used to lay down wetlines in areas where bare soil firebreaks can’t be installed; source of extra water |  |  |  |  |
|  | ATV’s, (4 Wheelers) | Helpful for large areas or rough terrain; can mount ATV water sprayers on them or light firelines |  |  |  |  |
| Equipment Items | Equipment Suggestions | Amount On-Hand | Amount Needed | Comments / Other Considerations | Available Day Of Burn |
| Supplies | Diesel & Gas mixture for torches | Fuel mixture is a 1:1 diesel:gas – on warmer days this can approach a 2:1 diesel:gas mixture |  |  |  |  |
|  | Matches or lighters | Used for lighting the torches; may be needed in emergencies to burn out a black area around yourself should one get trapped inside a burning area accidentally |  |  |  |  |
|  | Fuel (Not mixed) | Needed for motors on pumps, sprayers, or ATV’s |  |  |  |  |
|  | Drinking water | Needed to keep the fire crew hydrated and functioning |  |  |  |  |
|  | Toolkit / Fencing pliers / Other tools | Pliers may be needed to cut fences to allow vehicles to get to an escape; other tools for repairs on equipment |  |  |  |  |
| Communications | Weatherkit | Obtain on-site weather information & monitor weather parameters during the burn |  |  |  |  |
|  | Two-way radio(s) | Vital for communication between all crew members & the fireboss |  |  |  |  |
|  | NOAA Radio | Helpful to monitor weather especially if a front is predicted |  |  |  |  |
|  | Cellular phone | Fireboss should have a means of contacting emergency personnel if the need arises |  |  |  |  |
|  | GPS | Coordinates can be useful for emergency personnel if site is in a remote area |  |  |  |  |
| Safety Equipment | All cotton / Nomex clothing | Long sleeve shirts, pants - no cuffs, worn outside of boots; no rips, tears, or frays in clothing |  |  | All crew members |  |
|  | Cotton cap(s) / Helmet(s) | Long hair inside |  |  | All crew members |  |
|  | Leather gloves and boots | Gloves – no large cuffs; Boots – lace-up preferred; No sneakers |  |  | All crew members |  |
|  | Dust masks and goggles | Dust masks to filter ash & some smoke; goggles to protect eyes from heat & smoke irritation or when using power tools (leaf blowers, chainsaws) |  |  | All crew members |  |
|  | Face Protectors | Nomex fire resistant material for use on fireline to protect face from heat |  |  |  |  |
| Crew Members and Responsibilities – Do not burn until all precautions have been taken and all personnel on site are informed of the burn plan and their responsibilities during the burn. Have on-hand sufficient equipment and manpower needed to control the fire at all times. Ensure that all personnel are able to operate their assigned equipment. |
| FIREBOSS *** |  | Total number of crew members needed: |  |
| ***The fireboss will be the sole leader and coordinator of all prescribed burning activities. If the fireboss is not satisfied with the firebreak preparation, fire prescription, personnel, weather conditions, or other aspects of safety, then the burn shall be postponed. |
| Name | Responsibility (i.e. ignition, suppression, spotters, flager, etc.) | Reviewed w/Crew (Y/N) |
|  | Fire Weather and Smoke Observation |  |
| Conducting the Burn | Projected Date of Burn | From: |  | To: |  |
| Ignition Plan – Describe sequence of ignition for both burned firebreaks and main fire. Include details of ignition plan on burn plan map. |
| Plan of Action should the fire escape or wind changes directions |
| Burn Plan Map – (Include legend with north arrow, smoke management considerations, archaeological/cultural resource sites, roads, firebreaks, utilities, water sources, ingress/egress routes for emergency vehicles, ignition plan, areas not to be burned, facilities and other items as needed.) |
| “Mop-Up” After Burning Maintenance shall include “mop-up” or monitoring of the burned site and adjacent areas until ash, debris and other consumed material is at pre-burn temperatures. Be aware that stumps, snags, fence posts, and manure piles may smolder for several days after the burn. “Mop-up” actions may include drenching with water or fire retardant, smothering with a covering of soil or sand, or flapping and raking the fuels apart. “Mop-up” procedures need to continue until all “hot spots” have been extinguished. Be especially careful with burning materials near the perimeter of the burned area and move burning or smoldering materials to a safe area inside the burned area. | Responsibility |
| Maintain close observation of the burned area until the fire is completely extinguished. |  |
| Maintain contact with the weather station until the fire is extinguished. |  |
| Take immediate positive action to ensure safety of the fire should a dangerous change in the weather conditions occur. |  |
| Check entire perimeter of the burn area for firebrand sources, hollow trees, poles and posts, smoldering brush and log piles, cow chips, and heavy mulch areas. Make sure the entire area is “safe”. |  |
| Post-Burn Notification: After the burn is completed and all “mop-up” has been accomplished, the list of people and agencies notified before the burn should again be notified that the burn is complete. This will ensure that if a wildfire or accidental escape (poor “mop-up”) occurs, help will be summoned immediately |  |
| OTHER ITEMS: |  |
| Post Burn Management – Management needed after the burn in order to meet objectives. Include any recommendations or considerations needed for invasive species. |
| Days Since Rain |  | Actual Weather Conditions at time of Burn – Record periodically during time of burn |
| Time | Wind Speed | Wind Direction | Relative Humidity | Air Temperature | Source of Data |
| Time of Observation: | Smoke Monitoring Observations: |
| This Prescribed Burn plan was designed by |
| Planner | Date |
| NRCS Certification Information – (Refer to General Manual 190, Part 413, Subpart B for NRCS Policy and Job Approval Authority. Planners should review their individual job approval authority for certification levels) |
|  | Select Appropriate Categories for Planned Burn | For each Category, select appropriate Certification Level of person planning burn |
| Class: (check one) | 1 2 3 4 5 6 7 | 1 2 3 4 5 6 7 |
| Size of Area: (check one) | < 100 acres 100 to 640 acres >640 acre | < 100 acres 100 to 640 acres >640 acre |
| Vegetation: (check appropriate box) | Non-Volatile Herbaceous Non-Volatile Herbaceous and Woody Non-Volatile Herbaceous and Woody+ Volatile herbs < 4 feet tall. Non-Volatile Herbaceous + Volatile Woody > 4 feet tall + Dense Volatile Woody All Types of Fuels | Non-Volatile Herbaceous Non-Volatile Herbaceous and Woody Non-Volatile Herbaceous and Woody+ Volatile herbs < 4 feet tall. Non-Volatile Herbaceous + Volatile Woody > 4 feet tall + Dense Volatile Woody All Types of Fuels |
| Terrain: (check appropriate box) | 5% slope or less. 10% slope or less. More than 10% No Slope restriction | 5% slope or less. 10% slope or less. More than 10% No Slope restriction |

| Items within the burn plan that are in red are responsibility of client. Planner may assist where needed. Some items will be documented day of burn. |
| --- |
| Client Certification |
| This is to certify that the Natural Resources Conservation Service has informed me that I could be liable for damages resulting from this prescribed burn and the cost of fire suppression should the fire escape from the designated area. I also certify that it is my responsibility to be familiar with and comply with state burning laws. |
| Client | Date |

Operations and Maintenance:

The fire boss must:

- Review the burn plan with the burn fire crew prior to the burn.

- Conduct a test fire prior to the burn to determine if the fire is going to accomplish the objectives in a safe manner.

- Be in charge of the burn at all times.  Continually assess the progress of the burn, make needed adjustment, keep the fire crew informed of decisions, progress, and changes made during the fire.

- Be highly mobile.

- Monitor fire lines continuously.

- Assure that prescribed burn is within prescription and shut down the fire when fire gets out of prescription.

- The fire boss must maintain close observation of the burn area until the fire is completely extinguished.  Stumps and dry manure may smolder for several days after the burn.  Be especially careful with burning material that is within 50 feet of the perimeter of the burn area.

- Prescribed burning can be physically strenuous.  All crewmembers should be in good physical condition to enable them to perform all necessary assigned tasks.

- All firefighting equipment should be inventories and tested prior to starting fire.

I agree to install this practice as designed and planned.  I assume all liability for damages resulting from this prescribed burn and the cost of fire suppression should the fire escape from the designated area.

| Client: |  | Date: |  |
| --- | --- | --- | --- |

This practice is designed and planned according to NRCS NM Standards and Specifications.

| Conservationist: |  | Date: |  |
| --- | --- | --- | --- |

This practice is designed and planned according to NRCS NM Practice job approval authority.

| Reviewing Conservationist: |  | Date: |  |
| --- | --- | --- | --- |

This practice was installed and maintained in accordance with this job sheet.

| Completed by: |  | Date: |  |
| --- | --- | --- | --- |

PRESCRIBED BURN GO/NO-GO CHECKLIST

| A. | Has the burn unit experienced unusual drought conditions or does it contain above normal fuel loadings which were not considered in the prescription development? If NO proceed with checklist below, if YES go to item B. | YES | NO |
| --- | --- | --- | --- |
| B. | Has the prescribed fire plan been reviewed and an amendment and technical review been completed; or has it been determined that no amendment is necessary? If YES to any, proceed with checklist below, if NO, STOP. |  |  |

| YES | NO | QUESTIONS |
| --- | --- | --- |
|  |  | Are ALL pre-burn prescription parameters met? |
|  |  | Are ALL smoke management specifications met? |
|  |  | Has All required current and projected fire weather forecast been obtained and are they favorable? |
|  |  | Are ALL planned operations personnel and equipment on-site, available, and operational? |
|  |  | Has the availability of ALL contingency resources been checked and are they available? |
|  |  | Have ALL personnel been briefed on the project objectives, their assignment, safety hazards, escape routes, and safety zones? |
|  |  | Have all the pre-burn considerations identified in the prescribed Fire Plan been completed or addressed? |
|  |  | Have ALL the required notifications been made? |
|  |  | Are ALL permits and clearances obtained? |
|  |  | In your opinion, can the burn be carried out according to the Prescribed Fire Plan and will it meet the planned objective? |

If all the questions were answered “YES” proceed with a test fire.  Document the current conditions, location, and results.

| Burn Boss | Date |
| --- | --- |